## Slide 1
In the decoupling function, some inventory may be stored between each production process to act as a buffer. True
The economic order quantity helps one estimate the optimal number of units to purchase with each order. True
One reason inventory is required is the uneven flow of resources through a company. True
The reorder point occurs during a stock out. False
The purpose of the EOQ model is to achieve a balance between the cost of holding inventory and the cost of stock outs. False
The production run model is useful when a firm purchases inventory that is delivered over a period of time. True
One of the assumptions of the basic EOQ model is that the receipt of inventory is instantaneous. True
In a quantity discount model, the purchase cost or material cost must be included in the total cost calculation. True
The two fundamental decisions that you have to make when controlling inventory are: (1) how much to order, and (2) how much money to spend. False

## Slide 2
1. The "point at which to reorder" depends directly on which of the following?
A) EOQ
B) ordering cost
C) lead-time
D) storage costs
2. The daily demand of cars is 7 cars, and 4 days must be allowed between order placement and order receipt. Find ROP (reorder point).
a. 28
b. 32
c. 24
d. 11

## Slide 3
a. 11
b. 30
c. 160
d. 220
3. Consider the material structure tree for item A below. If 20 units of A are needed, how many units of D are needed?
3. Using the standard normal distribution table, the Z value for 96% service level is 1.75.
Standard deviation during lead time is 100, then the safety stock will be
150
175
200
160

## Slide 4
4. Using the standard normal distribution table, the Z value for 96% service level is 1.75. Standard deviation during lead time is 100, If average daily demand during lead time is 300, then ROP
575
475
375
450

## Slide 5
1. Flemming Accessories produces paper slicers used in offices and in art stores. The minislicers has been one of its most popular items: Annual demand is 6,750 units and is constant throughout the year. Kristen Flemming, owner of the firm, produces the minislicers in batches. On average, Kristen can manufacture 125 minislicers per day. Demand for these slicers during the production process is 30 per day. The setup cost for the equipment necessary to produce the minislicers is $150. Carrying costs are $1 per minislicers per year.
a. How many minislicers should Kristen manufacture in each batch?
b. How many orders per year are needed with the optimal policy?
c. What is the average inventory if costs are minimized?
d. If lead time is 2 days, what should be the re-order point?
e. What will the minimum total annual cost?

## Slide 8
Solution:

## Slide 9
A Computer Company sells a desktop computer that is popular among gaming enthusiasts. In the past few months, demand has been relatively consistent, although it does fluctuate from day to day. The company orders the computer cases from a supplier. It places an order for 5,000 cases at the appropriate time to avoid stockouts. The demand during the lead time is normally distributed, with a mean of 1,000 units and a standard deviation of 200 units. The holding cost per unit per year is estimated to be $4. How much safety stock should the company carry to maintain a 96% service level? What is the reorder point?
Find the size of Safety Stock.
What will be the re-order point?
What would the total annual holding cost be if this policy is followed?