## Slide 1: The description of the Plane Curvilinear Motion by the Polar Coordinates
Lecture VI
Polar coordinates

## Slide 2: Plane Curvilinear Motion – Polar Coordinates
Here, the curvilinear motions measurements are made by the radial distance (r) from a fixed pole and by an angular measurement (q) to the radial line.
The x-axis is used as a reference line for the measurement of q.
er & eq are the unit vectors in r-direction and q-direction, respectively.

## Slide 3: Polar Coordinates – Position & Velocity
Note: from (b), der is in the positive q-direction and deq in the negative r-direction
The position vector of the particle:
The velocity is:
?
(after dt)
(after dt)

## Slide 4: Polar Coordinates – Velocity (Cont.)
Thus, the velocity is:
Its magnitude is:
Due to rotation of r
Due to the rate at which the vector stretches

## Slide 5: Polar Coordinates - Acceleration
Rearranging,
Its magnitude is:
Coriolis acceleration
Centripetal acceleration

## Slide 6: Polar Coordinates – Circular Motion
For a circular path: r = constant
Note: The positive r-direction is in the negative n-direction, i.e. ar = - an

## Slide 7: Polar Coordinates Exercises

## Slide 8: Exercise # 1
As the hydraulic cylinder rotates around O, the exposed length l of the piston rod is controlled by the action of oil pressure in the cylinder. If the cylinder rotates at the constant rate q˙= 60 deg/s and l is decreasing at the constant rate of 150 mm/s, calculate the magnitudes of the velocity v and acceleration a of end B when l = 125 mm.

## Slide 9: Exercise # 2
The rob OA is rotating in the horizontal plane such that θ = (t3) rad. At the same time, the collar B is sliding outwards along OA so that r = (100t2)mm. If in both cases, t is in seconds, determine the velocity and acceleration of the collar when t = 1s.

## Slide 10: Exercise # 3
Due to the rotation of the forked rod, ball A travels across the slotted path, a portion of which is in the shape of a cardioids, r = 0.15(1 – cos θ)m where θ is in radians. If the ball’s velocity is v = 1.2m/s and its acceleration is 9m/s2 at instant θ = 180°, determine the angular velocity and angular acceleration of the fork.

## Slide 11: Exercise # 4
At the bottom of a loop in the vertical (r-q) plane at an altitude of 400 m, the airplane P has a horizontal velocity of 600 km/h and no horizontal acceleration. The radius of curvature of the loop is 1200 m. For the radar tracking at O, determine the recorded values of r˙ , r¨, q˙, and q ¨.

## Slide 12: Approach to Space Curvilinear Motion
Rectangular Coordinates (x, y, z)
Cylindrical Coordinates (r, q, z)

## Slide 13: Approach to Space Curvilinear Motion
Spherical Coordinates (r, q, f)

## Slide 14: Approach to Space Curvilinear Motion (Exercise)
The motion of box B is defined by the position vector r = {0.5sin(2t)i + 0.5cos(2t)j – 0.2tk} m, where t is in seconds and the arguments for sine and cosine are in radians (π rad = 180°). Determine the location of box when t = 0.75 s and the magnitude of its velocity and acceleration at his instant.

## Slide 15: Approach to Space Curvilinear Motion (Exercise)
The box slides down the helical ramp which is defined by r = 0.5 m, q = (0.5t3) rad, and
z = (2 – 0.2t2) m, where t is in seconds. Determine the magnitudes of the velocity and acceleration of the box at the instant q = 2p rad.

## Slide 16: Approach to Space Curvilinear Motion (Exercise)
The base structure of the fire truck ladder rotates about a vertical axis through O with a constant angular velocity  = 10 deg/s. At the same time, the ladder unit OB elevates at a constant rate ϕ˙ = 7 deg/s, and section AB of the ladder extends from within section OA at the constant rate of 0.5 m/s. At the instant under consideration, ϕ = 30, OA = 9 m, and AB = 6 m. Determine the magnitudes of the velocity and acceleration of the end B of the ladder.