## Slide 1: Curvilinear Motion
Lecture IV

## Slide 2: Topics Covered in Curvilinear Motion
Plane curvilinear motion
Coordinates used for describing curvilinear motion
  Rectangular coords
  n-t coords
  Polar coords

## Slide 3: Plane curvilinear Motion
Studying the motion of a particle along a curved path which lies in a single plane (2D).
This is a special case of the more general 3D motion.
3D

## Slide 4: Plane curvilinear Motion – (Cont.)
If the x-y plane is considered as the plane of motion; from the 3D case, z and j are both zero, and R becomes as same as r.
The vast majority of the motion of particles encountered in engineering practice can be represented as plane motion.

## Slide 5: Coordinates Used for Describing the Plane Curvilinear Motion
Rectangular coordinates
Normal-Tangential coordinates
Polar coordinates
y
x
P
t
n
PA
PB
PC
t
n
t
n
y
x
P
r
q
q
r
Path
Path
Path
O
O

## Slide 6: Plane Curvilinear Motion – (Displacement)
Note: Since, here, the particle motion is described by two coordinates components, both the magnitude and the direction of the position, the velocity, and the acceleration have to be specified.
or r(t)+Dr(Dt)
Ds
(Dt)
Note: If the origin (O) is changed to some different location, the position r(t) will be changed, but Dr(Dt) will not change.
Actual distance traveled by the particle (it is s scalar)
The vector displacement of the particle

## Slide 7: Plane Curvilinear Motion – (Velocity)
Average velocity (vav):
Instantaneous velocity (v): as Dt approaches
zero in the limit,
Note: vav has the direction of Dr and its magnitude equal to the magnitude of Dr divided by Dt.
Note: the average speed of the particle is the scalar Ds/Dt. The magnitude of the speed and vav approach one another as Dt approaches zero.
Note: the magnitude of v is called the speed, i.e. v=|v|=ds/dt= s..
Note: the velocity vector v is always tangent to the path.

## Slide 8: Plane Curvilinear Motion – (Acceleration)
Average Acceleration (aav):
Instantaneous Acceleration (a): as Dt approaches
zero in the limit,
Note: aav has the direction of Dv and its magnitude is the magnitude of Dv divided by Dt.
Note: in general, the acceleration vector a is neither tangent nor normal to the path. However, a is tangent to the hodograph.
C
Hodograph
P
P
V1
V2
V1
V2
a1
a2

## Slide 9: The description of the Plane Curvilinear Motion in the Rectangular Coordinates (Cartesian Coordinates)

## Slide 10: Plane Curvilinear Motion - Rectangular Coordinates
y
x
P
Path
O
j
i
r
v
vy
vx
q
a
ay
ax
P
Note: the time derivatives of the unit vectors are zero because their magnitude and direction remain constant.
Note: if the angle q is measured counterclockwise from the x-axis to v for the configuration of the axes shown, then we can also observe that dy/dx = tanq = vy/vx.

## Slide 11: Plane Curvilinear Motion - Rectangular Coordinates (Cont.)
The coordinates x and y are known independently as functions of time t; i.e. x = f1(t) and y = f2(t). Then for any value of time we can combine them to obtain r.
Similarly, for the velocity v and for the acceleration a.
If is a given, we integrate to get v and integrate again to get r.
The equation of the curved path can obtained by eliminating the time between x = f1(t) and y = f2(t).
Hence, the rectangular coordinate representation of curvilinear motion is merely the superposition of the components of two simultaneous rectilinear motions in x- and y- directions.

## Slide 12: Plane Curvilinear Motion - Rectangular Coordinates (Cont.) – Projectile Motion
x
Path
y
q
vo
(vx)o = vo cosq
(vy)o = vo sinq
g
v
vy
vx
v
vy
vx
Note:
If final velocity is not needed, equations (2) and (4) would not be needed

## Slide 13: Exercises

## Slide 14: Exercise # 1
The velocity of a particle is v = {3i + (6 - 2t)j} m/s, where t is in seconds. If r = 0 when t = 0, determine the displacement of the particle during the time interval t = 1 s to t = 3 s. Also, determine the acceleration at t = 3 s.

## Slide 15: Exercise # 2

## Slide 16: Exercise # 3
A roofer tosses a small tool to the ground. What minimum magnitude v0 of horizontal velocity is required to just miss the roof corner B? Also determine the distance d.

## Slide 17: Exercise # 4
The chipping machine is designed to eject wood at chips vO = 7.5 m/s. If the tube is oriented at 30° from the horizontal, determine how high, h, the chips strike the pile if they land on the pile 6 m from the tube.

## Slide 18: Exercise # 5
The track for this racing event was designed so that the riders jump off the slope at 30°, from a height of 1m. During the race, it was observed that the rider remained in mid air for 1.5 s. Determine the speed at which he was traveling off the slope, the horizontal distance he travels before striking the ground, and the maximum height he attains. Neglect the size of the bike and rider.

## Slide 19: Exercise # 6
A model rocket is launched from point A with an initial velocity of 86 m/s. If the rocket’s descent parachute does not deploy and the rocket lands 104 m from A, determine (a) the angle that forms with the vertical, (b) the maximum height h reached by the rocket, (c) the duration of the flight.

## Slide 20: Exercise # 7
Determine the minimum initial velocity v0 and the corresponding angle q0 at which the ball must be kicked in order for it to just cross over the 3-m high fence.